## Slide 1: System Verilog Lab 05
Asif Ansari

## Slide 2: LAB12: The Cache Controller
Difficulty: Easy Concepts: Virtual Methods, Compile vs Runtime Binding, Polymorphism, Safe Downcasting
Every instruction the CPU executes touches memory. A register load, a stack push, a pointer chase — each one becomes a read or a write on the memory bus. Main memory is large and slow. If the CPU waited for DRAM on every access, it would spend most of its time stalled, doing nothing.
So the SoC places a cache between the CPU and main memory: a small, fast SRAM that holds copies of recently accessed data. When the CPU reads an address, the cache checks whether it already has that data. If it does — a hit — the data comes back in one cycle. If it does not — a miss — the cache fetches an entire line (64 bytes) from main memory, installs it, and then returns the data. The next access to any byte in that line will be a hit.
The cache is direct-mapped: each memory address maps to exactly one cache line, determined by the address bits. A line has four fields:
Field | Width | Meaning
valid | 1-bit | Does this line hold real data?
dirty | 1-bit | Has this line been written since it was fetched?
tag | 32-bit | Which memory address does this line belong to?
data | 64 bytes | The actual cached data (one cache line)

## Slide 3: LAB12: The Cache Controller
Every memory access becomes one of four transaction types, and each one does something fundamentally different:
Read Hit — the address is in the cache and valid. Return the data. Latency: 1 cycle. Nothing else happens.
Read Miss — the address is not in the cache (or the line is invalid). The controller must fetch the line from main memory (latency: 100 cycles), install it in the cache (set valid = 1, dirty = 0, write the tag and data), and then return the data. If the line being replaced was dirty, it must be written back to main memory first.
Write Hit — the address is in the cache and valid. Update the data in place and mark the line dirty = 1. The write-back policy means the data is not sent to main memory yet — it will be written back only when the line is evicted.
Write Miss — the address is not in the cache. The controller must allocate a line (evicting a dirty line if necessary), fetch the old data from memory, apply the write, and mark the line dirty. This is the slowest path.
Every one of these four transactions shares common state: an address, a data payload, and a latency count. But each one's execute() does something completely different to the cache line. The controller must process a stream of transactions without knowing — or caring — which type each one is.

## Slide 4: LAB12: The Cache Controller
The Dispatcher Problem:
The first version of the cache controller testbench processed transactions like this:
if (txn_type == READ_HIT) process_read_hit(addr, data);
else if (txn_type == READ_MISS) process_read_miss(addr, data);
else if (txn_type == WRITE_HIT) process_write_hit(addr, data);
else if (txn_type == WRITE_MISS) process_write_miss(addr, data);
Four branches. Four separate functions. Every time architecture added a new transaction type — prefetch, cache-flush, invalidate — the if/else chain grew. Someone forgot to add the else if for cache-flush. The transaction was silently dropped. The test passed because nothing checked that it had been processed.
Architecture's mandate:
The controller must store every transaction in one queue, pull them out one at a time, and call execute(). Adding a new transaction type must not require changing the controller loop.

## Slide 5: LAB12: System Requirements
Task 1 — Build CacheLine. A standalone class representing one slot in the cache. Fields: valid, dirty, tag, data[64]. Must be constructable with a tag value and must be able to display its state.
Task 2 — Build CacheTransaction. The base class for all cache transactions. Fields: addr, data[64], latency. Must track how many transactions have been created across the entire simulation. Provides execute(CacheLine line) and identify(). Base execute() assumes a simple 1-cycle hit.
Task 3 — Build ReadHit extends CacheTransaction. A cache read that finds its data already present. Fastest path. No additional fields.
Task 4 — Build ReadMiss extends CacheTransaction. A cache read that must fetch the line from main memory. Must detect whether the replaced line needed writeback. Latency: 100 cycles.
Task 5 — Build WriteHit extends CacheTransaction. A cache write to a line already present. Updates the line and marks it appropriately. No additional fields.
Task 6 — Build WriteMiss extends CacheTransaction. A cache write that must allocate a line, potentially evicting a dirty resident. Must preserve the evicted line's state before overwriting. Latency: 100 cycles.
Task 7 — The non-virtual baseline. Store all four transaction types in a single base-handle array. Process them through one loop. Record and explain the output.
Task 8 — Fix the dispatch. Make the controller loop call the correct execute() and identify() for each transaction type. Do not modify the testbench.
Task 9 — Downcast safely. Extract the WriteMiss-specific data from the base-handle array. First attempt it unsafely. Then make it robust against reordering.

## Slide 6: LAB12: Key Learnings
virtual changes when the decision is made. Without it, the compiler picks the method at compile time from the handle type. With it, the simulator picks at runtime from the object type. The override exists either way — virtual decides who sees it.
The testbench does not change. Tasks 7 and 8 use identical testbench code. Only the base class changed. Callers program to the base interface; objects provide the implementation.
Non-virtual is the default for a reason. Virtual dispatch costs a vtable lookup per call. For internal helpers never called through a base handle, that cost is wasted. Make a method virtual only when you need polymorphic behavior.
Signature mismatch silently breaks the override. If a derived method has a different return type or argument list, it is not an override — it is a new method. The vtable still points to the base. There is no warning. Match the signature exactly.
Upcasting is implicit; downcasting is dangerous. Storing a WriteMiss in a CacheTransaction handle is always safe. Going the other way requires $cast, because the compiler cannot know at compile time what the object really is.
$cast is a question, not a command. It returns 1 if the object is compatible, 0 if not. Always check the return value. An unchecked $cast is no safer than a static cast.

## Slide 7: LAB13: The Eviction Log
Difficulty: Medium Concepts: Shallow and Deep Copy
The cache controller from LAB12 evicts dirty lines. When a WriteMiss hits a slot that already holds valid dirty data, it saves the old line into evicted_line before overwriting. The scoreboard uses this saved line to verify that the evicted data was written back to main memory correctly.
The eviction logic in WriteMiss.execute() looks like this:
if (line.valid && line.dirty) begin
      evicted_line = new();
      evicted_line.tag = line.tag;
      evicted_line.valid = line.valid;
      evicted_line.dirty = line.dirty;
      foreach (line.data[i]) evicted_line.data[i] = line.data[i];
      end
Field-by-field copy. Every scalar and every array element copied individually. It works. The scoreboard reads evicted_line after the transaction completes and finds the old tag, the old dirty bit, the old data. Everything matches.
Then the architecture team added a feature: line metadata. Each cache line now carries a pointer to a LineMetadata object that tracks access history - how many times the line has been read, how many times written, and the timestamp of the last access. The metadata is used by the replacement policy to decide which line to evict when the cache is full.
The CacheLine class gained one new field:
                LineMetadata meta;

## Slide 8: LAB13: The Eviction Log
    The field-by-field copy in WriteMiss dutifully copied it:
    evicted_line.meta = line.meta;
The scoreboard checked the evicted line's metadata immediately after eviction. It was correct. The test passed. Everyone moved on.
Two weeks later, the replacement policy test failed. The evicted line's metadata showed 47 reads and 12 writes. The reference model said it should show 3 reads and 1 write - the counts from before eviction. The metadata had kept counting after the eviction, because the evicted line and the live line were sharing the same LineMetadata object. The copy had copied the handle, not the object.

## Slide 9: LAB13: System Requirements
Task 1 - Build LineMetadata. Tracks read count, write count, and last access timestamp. Must be constructable and displayable.
Task 2 - Add a LineMetadata handle to CacheLine. Update CacheLine's constructor to create a fresh metadata object. Update display() to include metadata.
Task 3 - Write a copy() method on CacheLine that performs a shallow copy. Returns a new CacheLine with all fields duplicated - but handle fields copied as handles.
Task 4 - Testbench: create a CacheLine, increment its metadata counters, shallow-copy it, then continue incrementing the original's metadata. Print both. Observe that the copy's metadata changed too. Explain why.
Task 5 - Write a deep_copy() method on CacheLine that performs a deep copy. Handle fields must point to new, independent objects with the same values.
Task 6 - Testbench: repeat Task 4 using deep_copy(). Confirm the copy's metadata is frozen at the values it had when the copy was made. The original and the copy are fully independent.
Task 7 - Integrate into WriteMiss. Replace the field-by-field eviction copy with deep_copy(). Run the full polymorphic controller loop. Confirm the evicted line's metadata does not change when the live line's metadata is updated afterward.

## Slide 10: LAB13: Key Learnings
Shallow copy is the default trap. Copying an object field by field or through simple assignment gives you a new shell around shared guts. It works until someone mutates the shared part.
The bug is silent and delayed. The shallow copy passes every check at the moment of copying. The corruption appears later, when the original changes and the copy changes with it. The distance between cause and symptom makes it hard to debug.
Deep copy is a method, not a language feature. SystemVerilog has no built-in deep copy. You write it yourself. Every class that contains handles must decide: does copy() copy the handle or the object behind it?
The LAB12 copy worked by accident. It was shallow, but CacheLine had no handle fields. The moment a handle field was added, the copy broke. Code that works by accident breaks by surprise.

## Slide 11: LAB14: The Rigid Line
Difficulty: Medium Concepts: Parameterized classes
The cache controller from LAB13 works. The L1 cache runs at full speed. The eviction logic preserves metadata through deep copies. The scoreboard matches every writeback.
Then the architecture team added an L2 cache.
The L1 has 64-byte lines and 32-bit tags. The L2 has 128-byte lines and 48-bit tags. The replacement policy team wants to test both with the same controller logic, the same transaction types, the same scoreboard. The only things that differ are the dimensions.
The first engineer copied every class. CacheLine_L1 with byte data[64] and bit [31:0] tag. CacheLine_L2 with byte data[128] and bit [47:0] tag. Then CacheTransaction_L1 and CacheTransaction_L2. Then ReadHit_L1 and ReadHit_L2. Then WriteMiss_L1 and WriteMiss_L2. Each pair identical except for two numbers.
The LAB11 lesson was supposed to prevent this. Copy-paste killed the DMA driver. It is killing the cache controller the same way. A bug fix in ReadMiss_L1.execute() was never ported to ReadMiss_L2.execute(). The L2 scoreboard drifted for a week before anyone noticed.
Architecture's mandate:
One set of classes. The line size and tag width are parameters, not constants. A 64-byte/32-bit cache and a 128-byte/48-bit cache must come from the same source code. No duplication.

## Slide 12: LAB14: System Requirements
Task 1 - Parameterize LineMetadata. Add a type parameter that controls the timestamp type. Default: int unsigned. This allows a high-resolution cache to use longint unsigned without changing the class.
Task 2 - Parameterize CacheLine. Two value parameters: LINE_BYTES (default 64) and TAG_WIDTH (default 32). The data array size and tag field width must come from the parameters. The copy(), deep_copy(), and display() methods must work with any parameterization.
Task 3 - Parameterize CacheTransaction and all four derived classes (ReadHit, ReadMiss, WriteHit, WriteMiss) to work with the parameterized CacheLine. They must accept a CacheLine of matching parameterization.
Task 4 - Testbench: create an L1 configuration (CacheLine#(64, 32)) and an L2 configuration (CacheLine#(128, 48)). Run transactions against both. Confirm the line sizes and tag widths are correct for each.
Task 5 - Testbench: verify that static txn_count is tracked per specialization. L1 transactions and L2 transactions must have independent counters.
Task 6 - Testbench: attempt to pass an L2 CacheLine to an L1 transaction's execute(). Observe the compiler's response. Explain why parameterized type safety prevents this.

## Slide 13: LAB14: Key Learnings
Parameters eliminate duplication at the source. One CacheLine#(N, W) replaces every hand-copied variant. A bug fix in the template reaches every specialization.
Each specialization is a distinct type. CacheLine#(64, 32) and CacheLine#(128, 48) are not interchangeable. The compiler enforces this. You cannot accidentally pass an L2 line to an L1 transaction.
Static members are per-specialization. CacheTransaction#(64,32)::txn_count and CacheTransaction#(128,48)::txn_count are separate counters. Each specialization gets its own copy of static state.
Default parameters preserve backward compatibility. CacheLine#() behaves exactly like the old CacheLine from LAB13. Existing code does not break.
Type parameters generalize beyond values. LineMetadata#(longint unsigned) changes the timestamp precision without touching the logic. The class adapts to the type, not the other way around.